## Slide 2: What is Node-RED?
development tool
visual programming
flow-based
browser-based
wiring together HW devices, APIs, and online services
IoT
runtime built on Node.js (JavaScript runtime environment)

## Slide 3: How it works
node
  functionality
  inputs/outputs
a node can receive data and pass it to other nodes
nodes can be connected this way

## Slide 4: Environment

## Slide 5: Installation
install node.js
install node.red
OR via Docker

## Slide 7: What is MQTT?
messaging protocol
publish/subscribe based
bidirectional
lightweight
avoids direct connections between devices by relaying the data through a central server (broker)
easy to add new devices without having to change the existent infrastructure
no need for compatibility between the clients

## Slide 8: Publish & Subscribe
a device can publish messages to other devices
a device can subscribe to a topic to receive messages from it
PUBLISH
SUBSCRIBE

## Slide 9: Message
information exchanged between devices – commands or data
MESSAGE
MESSAGE

## Slide 10: Topic
the way you register interest for incoming messages or specify where you want to publish your messages
represented with strings separated by slashes “/” - slashes indicate the topic level
e.g.: home/office/lamp
TOPIC B MESSAGE
TOPIC A MESSAGE
DEVICE SUBSCRIBED TO TOPIC A
DEVICE SUBSCRIBED TO TOPIC B

## Slide 11: Broker
receives all messages, filters messages, publishes the messages to all subscribed clients
public/private
e.g.: Mosquitto broker
BROKER
DEVICE A
DEVICE B

## Slide 12: How it works
PUBLISH
PUBLISH
PUBLISH
SUBSCRIBE
SUBSCRIBE

## Slide 13: MQTT Quality of Service
value represents an agreement between the sender of a message and the receiver of a message
defines the guarantee of delivery for a specific message
3 possible values
  0 – at most once
  1 – at least once
  2 – exactly once

## Slide 14: Thank you for your attention!!
Petra Jankurová